## Slide 1
⚡
WEEK 2: DEEP ANALYSIS
STATE TRENDS · CUF · DEFICIT MAP · EOQ PREVIEW
Can Renewable Energy Solve India's Peak Demand Problem?
150 GW
Solar (Mar 2026)
~49%
Renewable Cap Share
0 GW
Solar at 8 PM Peak
~300 GWh
BESS Gap (national)
DATA: IDP CKAN API (5 datasets) + CICERO/CEA · All columns verified from IDP data dictionary
Sources: India Data Portal (ISB/BMGF) · CEA / Ministry of Power · NPP · CICERO/Robbie Andrew · All official Govt of India data

## Slide 2
DATA PIPELINE — IDP CKAN API + CICERO FALLBACK
All column names verified from IDP data dictionary pages · ckandev.indiadataportal.com/dataset/power
Installed Capacity Statewise
📌 IDP CKAN API /datastore/dump/
date, state_name, coal_cap, gas_cap, diesel_cap, lignite_cap,
nuclear_cap, hydro_cap, res_cap
NPP · Monthly · 2017–2025
Daily Renewable Generation
📌 IDP CKAN API /datastore/dump/
date, state_name, region, wind_energy, solar_energy,
other_renewable_energy, total_renewable_energy
CEA DGR · Daily · 2019–2025
Energy Req & Availability
📌 IDP CKAN API /datastore/dump/
month, state_name, state_code,
energy_requirement, energy_availability
CEA · Monthly · 2019–2023
Daily Coal Stocks
📌 IDP CKAN API /datastore/dump/
date, state_name, capacity, daily_requirement,
total_stock, stock_days, plf_prcnt, is_critical
NPP · Daily · 2014–2025
Daily Power Outage
📌 IDP CKAN API /datastore/dump/
date, state_name, station_type, power_station,
monitored_capacity, outage_capacity
NPP · Daily · 2014–2025
Monthly Capacity (national)
📌 CICERO/CEA CSV
YYYYMM, Coal_Lignite, Gas, Nuclear, Hydro,
Small_hydro, Wind, Biomass, Solar
CEA via Robbie Andrew · Monthly · 1947–2026
Loader: Method 1 → /datastore/dump/<id>?bom=True (full CSV) | Method 2 → /api/3/action/datastore_search (paginated 10k rows) | Method 3 → CICERO CSV
Sources: India Data Portal (ISB/BMGF) · CEA / Ministry of Power · NPP · CICERO/Robbie Andrew · All official Govt of India data

## Slide 3
NATIONAL CAPACITY MIX — THE RENEWABLE REVOLUTION
CEA Monthly Installed Capacity · CICERO mirror · YYYYMM, Coal_Lignite, Solar, Wind, Hydro, Nuclear (all in MW)
Coal+Lignite
170 GW
229 GW
Large Hydro
42 GW
51 GW
Nuclear
5.8 GW
8.8 GW
Wind
25 GW
56 GW
Solar
4 GW
150 GW
Biomass+SHP
11 GW
15 GW
2015
2026
RENEWABLE SHARE OF INSTALLED CAPACITY
~49%
☀️ Solar: 4 → 150 GW
37× in 10 years
World's fastest buildout
💨 Wind: 25 → 56 GW
2× growth · Slowing (land/grid constraints)
⚫ Coal share: 59% → 47%
Absolute GW still growing (+35%)
Phase-out needs storage solution
⚡ Total: 280 → 480+ GW
But generation mix still 70%+ fossil
Capacity ≠ Generation (CUF gap)
Sources: India Data Portal (ISB/BMGF) · CEA / Ministry of Power · NPP · CICERO/Robbie Andrew · All official Govt of India data

## Slide 4
STATE-WISE CAPACITY — WHO HAS WHAT? (IDP: coal_cap, hydro_cap, res_cap)
IDP dataset: installed_statewise · Columns: date, state_name, coal_cap, gas_cap, nuclear_cap, hydro_cap, res_cap (MW)
Rajasthan
43.2 GW RES
Gujarat
24.1 GW RES
Karnataka
22.4 GW RES
Tamil Nadu
22.2 GW RES
Andhra Pradesh
19.3 GW RES
Maharashtra
18.6 GW RES
Madhya Pradesh
15.1 GW RES
Telangana
11.8 GW RES
Uttar Pradesh
10.2 GW RES
Himachal Pradesh
0.5 GW RES
RES
Coal
Hydro
☀️ Geographic Concentration
Top 5 states = ~75% of all RES capacity
Rajasthan alone = ~28% of solar
⚡ Demand Mismatch
UP + MH + Delhi = 40%+ of national demand
But only ~10% of RES capacity
Requires massive grid investment
🔌 Transmission Bottleneck
Inter-state lines saturated in summer
Grid loss: 2-5% of renewable power
→ Effective deficit higher than reported
IDP API call: /datastore/dump/4ef9b444
columns: res_cap = Solar+Wind+SHP+Biomass aggregate (MW)
Sources: India Data Portal (ISB/BMGF) · CEA / Ministry of Power · NPP · CICERO/Robbie Andrew · All official Govt of India data

## Slide 5
DAILY RENEWABLE GENERATION — SEASONALITY & STATE LEADERS
IDP: daily_renewable · Columns: date, state_name, wind_energy, solar_energy, total_renewable_energy (MU)
Jan
Feb
Mar
Apr
May
Jun
Jul
Aug
Sep
Oct
Nov
Dec
Solar MU/day
Wind MU/day
Peak demand season
☀️ Top Solar Gen States
▸ Rajasthan
34.8 BU
▸ Gujarat
20.1 BU
▸ Karnataka
17.4 BU
▸ Tamil Nadu
12.2 BU
▸ Andhra Pradesh
15.6 BU
💨 Top Wind Gen States
▸ Tamil Nadu
39.2 BU
▸ Gujarat
27.8 BU
▸ Rajasthan
22.1 BU
▸ Andhra Pradesh
18.5 BU
▸ Karnataka
14.3 BU
Wind peaks Jul-Sep (monsoon)
Solar peaks Mar-May
BUT peak demand = Apr-Jun + Oct
→ Timing mismatch confirmed
Sources: India Data Portal (ISB/BMGF) · CEA / Ministry of Power · NPP · CICERO/Robbie Andrew · All official Govt of India data

## Slide 6
ENERGY DEFICIT MAP — WHERE IS POWER SCARCE?
IDP: energy_req_avail · Columns: month, state_name, energy_requirement, energy_availability (MU)
Maharashtra
0.1%
Telangana
0.2%
West Bengal
0.6%
Odisha
1.1%
Jharkhand
1.9%
Uttar Pradesh
2.4%
Bihar
3.1%
Arunachal Pradesh
4.2%
Meghalaya
4.7%
Himachal Pradesh
5.1%
Manipur
6.8%
Jammu & Kashmir
8.2%
Deficit % of energy requirement (avg 2019–2023)
📉 Economics of Deficit
Energy deficit formula:
Req - Avail = deficit_mu
J&K deficit (2022):
~590 MU / year
UP deficit (2022):
~2,100 MU / year
Est. GDP loss rate:
Rs 5,000 / MU unmet
DWL = area under
demand curve above supply
🔑 Thesis Connection
IDP data shows deficit is concentrated in
north/northeast India — precisely where
transmission from solar-rich Rajasthan
is most constrained.
Renewables built in wrong geography.
deficit_mu = energy_requirement - energy_availability
deficit_pct = deficit_mu / energy_requirement × 100
Source: IDP resource c8defaeb · CEA monthly state-level
Sources: India Data Portal (ISB/BMGF) · CEA / Ministry of Power · NPP · CICERO/Robbie Andrew · All official Govt of India data

## Slide 7
COAL STOCKS — EOQ PREVIEW (IDP: stock_days, plf_prcnt, is_critical)
IDP: coal_stocks · Columns: daily_requirement, total_stock, stock_days, normative_stock_days, plf_prcnt, is_critical (22 fields total)
Jan
2021
Apr
Jul
Oct
Jan
2022
Apr
Jul
Oct
7-day CRITICAL
14-day safe
Avg Stock Days at Thermal Plants (2021–2022) · Crisis Period Highlighted
📦 EOQ MODEL (Week 3 Build)
D (Demand Rate)
daily_requirement (Th T/day)
H (Holding Cost)
~Rs 150/tonne/day (CEA estimate)
S (Order Cost)
~Rs 3 Cr / coal rake
Q* (EOQ)
= sqrt(2 × D × S / H)
ROP (Reorder Pt)
7-day stock = normative_stock_days
SS (Safety Stock)
normative_stock (Th T)
Oct 2021: stock_days < 4 at 100+ stations
Root cause: EOQ violated + rail supply disruption
Not actual coal shortage → supply chain failure
Sources: India Data Portal (ISB/BMGF) · CEA / Ministry of Power · NPP · CICERO/Robbie Andrew · All official Govt of India data

## Slide 8
THE CORE GAP — SOLAR IS ZERO AT 8 PM PEAK
CICERO: capacity data · IDP: daily_renewable · CEA Peak Demand (Annual Reports) · Column: wind_energy (MU)
2019
2020
2021
2022
2023
2024
2025
50 GW
100
150
200
250
Wind at 8pm (~25% CUF)
Must come from Coal/Hydro/BESS
Total Peak Demand
☀️ SOLAR CONTRIBUTION AT 8 PM = 0 GW (every year, every day)
🔋 BESS SIZING ESTIMATE
Solar installed (2025):
150 GW
Solar CUF (avg):
20%
Peak solar gen/day:
240 GWh
Store 50% for evening:
120 GWh/day
×4hr evening discharge:
30 GW capacity
BESS needed (national):
~300-500 GWh
India's BESS today:
~4 GWh
GAP FACTOR:
75-125×
Week 3: LP model will find optimal BESS + dispatch mix
Sources: India Data Portal (ISB/BMGF) · CEA / Ministry of Power · NPP · CICERO/Robbie Andrew · All official Govt of India data

## Slide 9
CAPACITY UTILISATION — CUF BY SOURCE & OUTAGE ANALYSIS
IDP: power_outage · Columns: monitored_capacity, outage_capacity · Derived: available_cap = monitored - outage
Source
Annual Avg CUF
Summer Peak
Monsoon
☀️ Solar
20%
24%
15%
💨 Wind
25%
18%
30%
⚫ Coal
58%
72%
48%
💧 Hydro
38%
52%
28%
☢️ Nuclear
82%
82%
82%
🔥 Gas
22%
35%
12%
🔧 Week 3 LP Model Connection:
available_capacity = monitored_capacity - outage_capacity (from IDP power_outage) → upper bound in dispatch LP
Solar CUF × installed_cap → generation constraint · Coal PLF must stay > technical minimum (40%)
Coal: PLF Falling
From 68% (2018) to 55% (2024)
Renewables displacing coal in daytime
But coal must run nights → min. PLF constraint
Solar: High CUF Months
Mar-May: CUF peaks to 24%+
Dec-Jan: drops to 12%
Seasonality drives storage requirement
Nuclear: Baseload Hero
82% CUF — most reliable source
Only 8.8 GW total → too little
Expansion takes 8-10 years
Sources: India Data Portal (ISB/BMGF) · CEA / Ministry of Power · NPP · CICERO/Robbie Andrew · All official Govt of India data

## Slide 10
WEEK 2 FINDINGS + WEEK 3 ROADMAP
01 ☀️ Solar: 150 GW — But CUF Only 20%
India needs 5 GW solar to equal 1 GW coal output. Geographic mismatch adds further efficiency loss.
02 ⚡ Evening Peak Gap: 200+ GW unmet by renewables
Solar = 0 at 8pm. Wind = 25% CUF. Thermal/hydro covers 95%+ of evening peak. BESS gap: 300-500 GWh.
03 🗺️ Geographic Mismatch Quantified
Rajasthan/Gujarat = 52% of solar. UP/MH = 40% of demand. Transmission is the constraint.
04 ⚫ Coal: stock_days = 4 (2021 Crisis) — EOQ Was Violated
IDP data shows daily_requirement vs total_stock per station. Week 3 EOQ model will find optimal Q*.
▶ WEEK 3 PLAN — ML MODELS + MBA TOOLS
SARIMAX/Prophet
Forecast peak demand 2025-2030
POSOCO daily, IDP ERA monthly
EOQ Model
Optimal coal buffer per station
IDP coal_stocks: daily_requirement, normative_stock_days
PuLP LP
Min-cost dispatch: solar+wind+coal+hydro+BESS
IDP outage: monitored_capacity - outage_capacity
K-Means
Cluster states by power profile
IDP statewise: coal_cap, res_cap, deficit_pct
Sources: India Data Portal (ISB/BMGF) · CEA / Ministry of Power · NPP · CICERO/Robbie Andrew · All official Govt of India data