## Slide 1
☀️
“
MBA Project · Operations + Economics
India Peak
Power
Week 2 · Deep Analysis
State Trends · CUF by Source · Deficit Map · Coal EOQ · Evening Peak Gap
150 GW
Solar Installed
~49%
Renewable Share
0 GW
Solar at 8 PM
75-125×
BESS Gap Factor
Data: India Data Portal (ISB/BMGF) · CEA · NPP · CICERO/Robbie Andrew · All official Govt of India

## Slide 2
INSTALLED CAPACITY MIX
Who Generates
India's Power?
480 GW
Total Installed (Mar 2026)
150 GW
Solar — 26× growth since 2015
~49%
Renewable share of capacity
Chart: 
| Coal+Lignite | Solar | Wind | Large Hydro | Nuclear | Gas+Diesel | Biomass+SHP
Capacity Mix | 229 | 150 | 56 | 51 | 9 | 27 | 15
480
GW
Total
Key Insight
Coal still largest single source at 48% but falling.
Solar+Wind = 43% of total — nearly equal to coal for first time.
But generation ≠ capacity. CUF of solar is 20% vs coal at 58%.
IDP / CICERO
Column: YYYYMM,
Coal_Lignite, Solar,
Wind, Hydro, Nuclear
(all in MW)
Data: India Data Portal (ISB/BMGF) · CEA · NPP · CICERO/Robbie Andrew · All official Govt of India

## Slide 3
CAPACITY TREND 2015-2026
The Renewable Revolution
Solar 37×, Wind 2× in 10 Years
Chart: 
| 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2021 | 2022 | 2023 | 2024 | 2025 | 2026
Solar (GW) | 4 | 9 | 19 | 27 | 35 | 40 | 55 | 67 | 83 | 100 | 125 | 150
Wind (GW) | 25 | 29 | 33 | 36 | 38 | 40 | 41 | 43 | 45 | 48 | 52 | 56
☀️
Rajasthan
Solar capital — 43 GW RES, 28% of India's solar
💨
Tamil Nadu
Wind capital — 39 BU wind generation, top generator
⚡
Karnataka
Most balanced — solar + wind + hydro all top-5
🏭
UP
Demand hub — 100 GW peak demand, only 16 GW RES
Geographic mismatch: Rajasthan generates, UP/MH consume — grid is the bottleneck
Data: India Data Portal (ISB/BMGF) · CEA · NPP · CICERO/Robbie Andrew · All official Govt of India

## Slide 4
SEASONALITY ANALYSIS
When Do Renewables Generate?
Solar & Wind vs Peak Demand Season
Chart: 
| Jan | Feb | Mar | Apr | May | Jun | Jul | Aug | Sep | Oct | Nov | Dec
Solar (MU/day) | 100 | 115 | 155 | 175 | 165 | 135 | 100 | 90 | 105 | 125 | 105 | 88
Wind (MU/day) | 130 | 115 | 100 | 85 | 95 | 165 | 250 | 265 | 235 | 155 | 120 | 115
Peak
Demand
Season
(Apr-Jun)
High
Demand
(Oct-Nov)
1
Diurnal
Solar = 0 at 8 PM
Evening peak unmet every day
2
Seasonal
Wind peaks Jul-Sep
Solar peaks Mar-May
But demand peaks Apr-Jun
3
Geographic
Rajasthan solar →
must reach UP demand
via congested grid
Data: India Data Portal (ISB/BMGF) · CEA · NPP · CICERO/Robbie Andrew · All official Govt of India

## Slide 5
ENERGY DEFICIT ANALYSIS
More Renewables = Less Deficit?
IDP: energy_requirement vs energy_availability by state
Chart: 
| [object Object] | [object Object] | [object Object] | [object Object] | [object Object] | [object Object] | [object Object]
Medium deficit | [object Object] | [object Object] | [object Object] | [object Object] | [object Object]
Low deficit / surplus | [object Object] | [object Object] | [object Object] | [object Object] | [object Object] | [object Object] | [object Object]
Higher RES share → Lower deficit
Rs 5,000
/MU unmet energy
Est. GDP loss rate
<1%
National deficit today
(was 12% in 2013)
J&K 8.2%
Highest deficit state
(IDP: energy_req - avail)
IDP col: energy_requirement, energy_availability (MU) · monthly · state-level
Data: India Data Portal (ISB/BMGF) · CEA · NPP · CICERO/Robbie Andrew · All official Govt of India

## Slide 6
CAPACITY UTILISATION FACTOR
CUF: Capacity is Not Generation
Solar 20% CUF means 5 GW solar = 1 GW coal output
Chart: 
| Solar | Wind | Coal | Hydro | Nuclear | Gas
Annual Avg CUF (%) | 20 | 25 | 58 | 38 | 82 | 22
Summer Peak CUF (%) | 24 | 18 | 72 | 52 | 82 | 35
Monsoon CUF (%) | 15 | 30 | 48 | 28 | 82 | 12
☀️ Solar 20%
Need 5 GW solar to replace 1 GW coal (at same output). Higher capex per unit generation.
💨 Wind 25%
Peaks in monsoon (Jul-Sep), lowest in summer peak season. Opposite of when needed.
⚫ Coal 58%
PLF falling from 68%→55% as renewables displace daytime. Still needed for nights.
☢️ Nuclear 82%
Most reliable. Only 8.8 GW — too small. 8-10 yr expansion timeline.
Data: India Data Portal (ISB/BMGF) · CEA · NPP · CICERO/Robbie Andrew · All official Govt of India

## Slide 7
COAL STOCKS & EOQ MODEL
Coal Inventory Crisis 2021
IDP: stock_days, daily_requirement, normative_stock_days
Chart: 
| Jan21 | Mar21 | May21 | Jul21 | Sep21 | Oct21 | Nov21 | Jan22 | Mar22 | May22 | Jul22 | Oct22
Stock Days | 22 | 18 | 14 | 10 | 12 | 4 | 5 | 6 | 9 | 12 | 16 | 20
CRITICAL (7 days)
SAFE (14 days)
2021
2022
EOQ MODEL (Week 3)
D
Demand Rate
daily_requirement (Th T/day)
S
Order Cost
~Rs 3 Cr / coal rake
H
Holding Cost
~Rs 150 / tonne / day
Q*
EOQ Formula
sqrt(2 × D × S / H)
ROP
Reorder Point
normative_stock_days
SS
Safety Stock
normative_stock (Th T)
Oct 2021: stock_days < 4 at 100+ stations
Not a coal shortage — a supply chain (EOQ) failure
Data: India Data Portal (ISB/BMGF) · CEA · NPP · CICERO/Robbie Andrew · All official Govt of India

## Slide 8
THE CORE THESIS — EVENING PEAK GAP
Solar = 0 GW at 8 PM Peak
Wind covers only 10-15 GW · Gap must be Thermal / BESS
Chart: 
| 2019 | 2020 | 2021 | 2022 | 2023 | 2024 | 2025
Thermal/Hydro needed (GW) | 178 | 180.5 | 191 | 205.2 | 212.7 | 220.5 | 227
Wind at 8pm ~25% CUF (GW) | 9 | 9.5 | 10 | 10.8 | 11.3 | 12.5 | 14
☀️ SOLAR = 0 GW at 8 PM (every year, every day)
🔋 BESS Sizing (2025)
Solar installed
150 GW
CUF (avg)
20%
Daily solar gen
240 GWh
Store 50% for PM
120 GWh
4-hr PM discharge
30 GW
BESS needed
~400 GWh
India today
~4 GWh
GAP FACTOR
75-125×
India's BESS Gap
Needed: ~400 GWh
Today: ~4 GWh
Data: India Data Portal (ISB/BMGF) · CEA · NPP · CICERO/Robbie Andrew · All official Govt of India

## Slide 9
WEEK 2 SUMMARY
Key
Findings
1
Solar: 26×
150 GW installed but CUF only 20%
5 GW solar = 1 GW coal at output level
2
Evening Gap
Solar = 0 at 8 PM. BESS gap: 75-125×
India needs 300-500 GWh storage
3
State Mismatch
Rajasthan=52% solar, UP=40% demand
Transmission is the binding constraint
4
Coal Crisis 2021
stock_days fell to <4 at 100+ plants
EOQ violated — supply chain failure
IDP CKAN API + CICERO · CEA · NPP
Week 3 — ML Models + MBA Tools
📈
SARIMAX / Prophet
Forecast peak demand 2025-2030
POSOCO daily · IDP ERA monthly
📦
EOQ Model
Optimal coal buffer per station
daily_requirement · normative_stock_days
🔧
PuLP LP
Min-cost dispatch mix
monitored_capacity - outage_capacity
🗂️
K-Means Clustering
Group states by power profile
coal_cap · res_cap · deficit_pct
🔋
BESS Sizing Model
GWh storage per state to close gap
solar_energy · wind_energy · peak demand
💡
Counterfactual
What if solar = 500 GW? Gap closes?
LP model + capacity expansion simulation
Data: India Data Portal (ISB/BMGF) · CEA · NPP · CICERO/Robbie Andrew · All official Govt of India