## Slide 1
📈
SARIMAX
Demand Forecast
📦
EOQ Model
Coal Inventory
🔧
PuLP LP
Dispatch Optimise
🗂️
K-Means
State Clustering
🔋
BESS Sizing
Storage Capacity
💡
Counterfactual
500 GW Solar?
“
MBA Project · Week 3 of 4
Week 3:
ML Models
+ MBA Tools
5 Quantitative Models · SARIMAX · EOQ · LP · K-Means · BESS
241 GW
2025 Peak Demand
~270 GW
2030 Forecast
4 Clusters
State Segments
300-500 GWh
BESS Needed
Data: India Data Portal (ISB/BMGF) · CEA · NPP · CICERO/Robbie Andrew · Models: SARIMAX · EOQ · PuLP LP · K-Means

## Slide 2
MODEL 1 — SARIMAX DEMAND FORECAST
Peak Demand Forecast 2025–2030
SARIMAX(2,1,1) fitted on CEA Annual Reports · 95% confidence interval
Chart: 
| 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2021 | 2022 | 2023 | 2024 | 2025
Historical Peak (GW) | 164 | 177 | 184 | 190 | 200 | 215 | 224 | 232 | 241 | 249 | 257
SARIMAX Forecast | 257 | 263 | 271 | 279 | 287 | 295
95% CI Upper | 264 | 274 | 286 | 299 | 312 | 326
95% CI Lower | 250 | 252 | 256 | 259 | 262 | 264
3.5%
Forecast CAGR 2025-30
~295 GW
2030 Peak Forecast
±31 GW
95% CI Width by 2030
+54 GW
Above today's 241 GW
Model: SARIMAX(2,1,1) trend='c' | Data: CEA Annual Reports + POSOCO | AIC-optimised orders
Data: India Data Portal (ISB/BMGF) · CEA · NPP · CICERO/Robbie Andrew · Models: SARIMAX · EOQ · PuLP LP · K-Means

## Slide 3
MODEL 2 — EOQ COAL INVENTORY
EOQ: Oct 2021 Was a Supply Chain Failure
stock_days < 4 at 100+ stations — not a coal shortage, an EOQ violation
Chart: 
| Jan21 | Mar21 | May21 | Jul21 | Sep21 | Oct21 | Nov21 | Jan22 | Mar22 | May22 | Jul22 | Oct22
Stock Days | 22 | 18 | 14 | 10 | 12 | 4 | 5 | 6 | 9 | 12 | 16 | 20
CRITICAL (7d)
SAFE (14d)
2021
2022
Oct 2021: 100+ stations
below 7-day critical
EOQ Formula (Week 3 Applied)
D
daily_requirement (Th T/day)
Demand rate from IDP
S
~Rs 3 Cr / coal rake
Ordering cost per shipment
H
~Rs 150 / T / day
Holding cost (storage + risk)
Q*
= sqrt(2 × D × S / H)
Optimal order quantity
ROP
normative_stock_days × D
Reorder trigger point
SS
normative_stock (Th T)
Safety stock buffer
If Q* followed: Oct 2021 crisis preventable
EOQ insight: supply chain, NOT coal shortage
Data: India Data Portal (ISB/BMGF) · CEA · NPP · CICERO/Robbie Andrew · Models: SARIMAX · EOQ · PuLP LP · K-Means

## Slide 4
MODEL 3 — LINEAR PROGRAMMING DISPATCH
LP: Minimum-Cost Dispatch Mix
PuLP solver · 7 sources · 4 carbon cap scenarios · 2025 peak demand = 241 GW
Chart: 
| No Cap | 180k T/hr | 140k T/hr | 100k T/hr
Coal | 200 | 170 | 120 | 70
Gas | 8 | 8 | 8 | 8
Nuclear | 7.2 | 7.2 | 7.2 | 7.2
Hydro | 33 | 33 | 33 | 33
Wind | 14 | 14 | 14 | 14
BESS | 1 | 1 | 1 | 1
Solar | 0 | 0 | 0 | 0
Cost vs Carbon Tradeoff
Scenario
Dispatch Cost
CO2
vs Baseline
No Cap
Rs 820 Cr/hr
180 kT CO2/hr
baseline
180k cap
Rs 850 Cr/hr
180 kT CO2/hr
+4%
140k cap
Rs 940 Cr/hr
140 kT CO2/hr
+15%
100k cap
Rs 1,120 Cr/hr
100 kT CO2/hr
+37%
LP Key Finding
Decarbonisation costs +37% without BESS.
With 300 GWh BESS, cost premium falls to <10%.
Data: India Data Portal (ISB/BMGF) · CEA · NPP · CICERO/Robbie Andrew · Models: SARIMAX · EOQ · PuLP LP · K-Means

## Slide 5
MODEL 4 — K-MEANS STATE CLUSTERING
4 State Clusters — 4 Policy Levers
K-Means · Features: RES share, coal cap, deficit % · k=4 (optimal silhouette score)
Chart: 
| RE Champions | Transition Leaders | Coal Dependent | Energy Starved
RES Share (%) | 65 | 43 | 24 | 13
Coal Cap (GW) | 9 | 13 | 21 | 2
Deficit (%) | 1 | 2 | 3 | 5
🏆
RE Champions (3 states)
Rajasthan · Karnataka · Gujarat
Maximise export
capacity. Build
inter-state lines.
⚫
Coal Dependent (5 states)
UP · Maharashtra · MP · Jharkhand
Mandate BESS.
Coal PLF floor.
RE transition plan.
🔄
Transition Leaders (4 states)
TN · AP · Telangana
Fast-track RES.
Grid upgrades.
Demand management.
⚡
Energy Starved (6+ states)
Bihar · HP · Northeast
Priority RE alloc.
Demand subsidy.
Grid access.
Data: India Data Portal (ISB/BMGF) · CEA · NPP · CICERO/Robbie Andrew · Models: SARIMAX · EOQ · PuLP LP · K-Means

## Slide 6
MODEL 5A — BESS SIZING PER STATE
How Much Storage Does Each State Need?
BESS (GWh) = min(50% solar daily gen × 0.88 RT eff, state evening peak × 4hr discharge)
Chart: 
| Rajasthan | Gujarat | Karnataka | Tamil Nadu | Andhra Pradesh | Maharashtra | Madhya Pradesh | Telangana | Uttar Pradesh | Punjab
BESS Needed (GWh) | 69 | 20 | 16 | 10 | 13 | 9 | 8 | 10 | 3 | 1
Solar covers >60%
Solar covers 30-60%
Solar covers <30%
Mostly thermal needed
Sizing Methodology
▸ Solar daily gen:
= solar_GW × 20% CUF × 8 hrs
▸ Storable energy:
= daily gen × 50% × 88% RT eff
▸ Evening need:
= peak_demand_GW × 20% × 4 hrs
▸ BESS needed:
= min(storable, evening need)
▸ BESS power:
= BESS_GWh ÷ 4 hr discharge
National Total Needed
~300–500 GWh
India today: ~4 GWh installed → Gap factor: 75-125×
Cost at Rs 40 Cr/MWh: ~Rs 12,000–20,000 Cr
vs annual deficit cost: ~Rs 30,000+ Cr → BESS is ROI positive
Data: India Data Portal (ISB/BMGF) · CEA · NPP · CICERO/Robbie Andrew · Models: SARIMAX · EOQ · PuLP LP · K-Means

## Slide 7
MODEL 5B — COUNTERFACTUAL ANALYSIS
What If India Hits 500 GW Solar?
Coal still needed at peak — but drops from 200 GW to ~70 GW at 8 PM
Chart: 
| 150 | 200 | 250 | 300 | 400 | 500
Nuclear+Hydro (GW) | 55 | 55 | 55 | 55 | 55 | 55
Wind at 8pm (GW) | 14 | 14.5 | 15 | 15 | 16 | 17
BESS Discharge (GW) | 1 | 8 | 16 | 24 | 40 | 58
Coal still needed | 200 | 170 | 120 | 80 | 75 | 70
500 GW
Govt Target
200 GW
Coal at 8pm TODAY
(150 GW solar)
~70 GW
Coal at 8pm with
500 GW solar + BESS
-65%
Coal reduction
at evening peak
Still ≠ 0
Coal cannot be eliminated
without 24/7 storage
500 GW solar shifts India from 'coal-dominant' to 'coal-backup' at peak — with adequate BESS
Data: India Data Portal (ISB/BMGF) · CEA · NPP · CICERO/Robbie Andrew · Models: SARIMAX · EOQ · PuLP LP · K-Means

## Slide 8
WEEK 3 — INTEGRATED FINDINGS
5 Models, 5 Answers
Thesis quantified: Renewables solve capacity, not peak timing — storage is the swing factor
✅
Can renewables solve capacity gap?
YES — 49% share, growing
Model: Donut (W2)
❌
Can renewables solve peak timing gap?
NO — Solar=0 at 8pm, BESS gap 75-125×
Model: LP + BESS Sizing
📈
What is the demand trajectory?
241→295 GW by 2030 (+3.5% CAGR)
Model: SARIMAX
⚠️
Where is coal supply risk?
Oct 2021: 100+ critical — EOQ violated
Model: EOQ Model
🗂️
Which states need what policy?
4 clusters — 4 different levers
Model: K-Means
💡
Does 500 GW solar solve it?
Reduces coal 200→70 GW at peak (not zero)
Model: Counterfactual
▶ Week 4: Cost-Benefit of BESS · Pigouvian Subsidy Model · LP with capacity expansion · Final Executive Report
Data: India Data Portal (ISB/BMGF) · CEA · NPP · CICERO/Robbie Andrew · Models: SARIMAX · EOQ · PuLP LP · K-Means

## Slide 9
“
THESIS CONFIRMED — WEEK 3
Renewables
Solved the
Capacity Gap.
But NOT the
Evening Peak.
Storage is the missing link.
5 MBA models confirm this across demand forecasting, inventory, dispatch, clustering, and capacity planning.
1
SARIMAX
241→295 GW by 2030
2
EOQ
Oct 2021 = supply chain, not coal
3
LP
Coal still 70-200 GW at 8pm
4
K-Means
4 clusters, 4 policy levers
5
BESS
300-500 GWh national storage needed
Week 4 next: Cost-benefit · Pigouvian subsidy · LP expansion · Final report
Data: India Data Portal (ISB/BMGF) · CEA · NPP · CICERO/Robbie Andrew · Models: SARIMAX · EOQ · PuLP LP · K-Means